## Slide 1
EVA – 6s: STAGE EVA – TRANSLATION TO STATION #4 (00:15)
IV | EV1 (CDR) | EV2 (MMP)
Record Observational notes when directed by EV crew Systems Check prior to station arrival Estimate time of arrival Compute estimate of minutes behind (projected minus planned arrival time) Compute estimate of timeline margin How Confident are you in your estimate (+/- min) | TRANSLATION (00:15) Correlate observation with active geophysical data Inspect targets of opportunity as appropriate Photograph features while driving if possible Monitor active regolith analysis data as appropriate Correlate active data sources with observations | TRANSLATION (00:15) Operate rover along preplanned route
Variable | EV1 (CDR) | EV2 (MMP)
O2 |  | 
Pressure |  | 
EMU Faults |  | 
Water |  | 
NOTE
In traversing from Station #3 to 4 the surface characteristics should change from the blocky Front material to a smoother mare material. The Traverse will pass along the south western edge of a secondary crater cluster. Things to look for during this portion of the traverse are the secondary crater deposits and their relationship to surrounding terrain and eastern edge of the debris flow from the Front. Photographic documentation of these features is desirable.

## Slide 2
EVA – 6s: STAGE EVA – STATION #4 ACTIVITIES (00:15)
IV | EV1 (CDR) | EV2 (MMP)
Record PET at Arrival Convey summary of tasks to be performed by each crew member Record number and type of samples identified for sampling (note any specific details as instructed by MMP) Confirm GO for CDR MRU activation once MCC approves | GEOPHYSICAL MRU EXPERIMENT (00:15) Egress Rover Unload MRU Select and place MRU at sampling site Configure MRU H8 (00:03) Relocate left side strap to secondary attachment √ Retrieve hammer from tool carrier Tighten Yaw Slider friction lock Check that sampler feet are leveled and aligned Release yaw line from overhead carabineer √ Remove core tube from external handle Translate to Yaw Joint PIP pin with yaw line in tow Check hardware clear of intended motion path and moving joints √ Check Yaw PIP pin (1) expanded Activate MRU H8 (00:02) Retrieve hook by opening lid of MRU Rotate drill clockwise to seat threads √ Anchor GeoArray to the surface by driving Anchor End Effector through Anchor Hole Disconnect Power Driver from Anchor End Effector by rotating CCW √ Connect Powered Driver to a Seismic Sensor End Effector check that both are aligned √ Check for confirmation to activate MRU | GEOPHYSICAL SAMPLING (00:15) Park and Egress rover Unload Sampling MRU and camera Make Observations while photo documenting Report site context description (00:03) Environmental conditions (depth, current strength/direction, temperature, visibility) Unit descriptions (distinguishing features, unit relations and orientations) Variances from precursor data Other notable features Worksite Setup / Sample Prep (00:02) Set sampling markers next to candidate samples √ Each candidate samples are photographed Collect Samples (00:02) Connect Manual Driver to Rock End Effector, pushing until Latch clicks into place Remove Manual driver and effector from Sampling MRU Squeeze and hold handle of Manual Driver while placing over sample of interest Release handle, capturing sample inside End Effector √ Stow End Effector in Sample MRU Repeat Sampling procedures until desired samples are collected
NOTE
Check Mission Log for MCC Activation Criteria PRIOR to Activation
CAUTION
Avoid touching End Effectors to minimize contamination Latch may over extend when clicking into place
Sample ID | Container ID | Sample type (lvl of alt – H/M/L)

## Slide 3
EVA – 6s: STAGE EVA – STATION #4 ACTIVITIES (00:15) CONT.
IV | EV1 (CDR) | EV2 (MMP)
Confirm MRU system checkout complete Confirm each sample is collected and stowed Provide MCC with a quick verbal status update of activities performed at Station #4. Compute estimate of minutes behind (projected minus planned end time of Station #4 activities) Do you think the EV crew will finish Station #4 on time? If not, what is your estimated end time? Systems Check prior to station departure Record PET at Departure | GEOPHYSICAL MRU EXPERIMENT (00:15) Perform system checkout √ System state variables Confirm System Checkout Clean-Up Worksite √ MRU Systems on data collection standby mode √ Use wrench and vise to tighten 3rd stem joint Stow hardware tools in MRU containment bag Stow Hardware √ All tools stowed and secured in containment bag Stow containment bag on Rover √ Place core stems on Z struts Mount rover (Fasten Seatbelt) Verify rover scientific instruments active Verify following in good config prior to commencing translation (00:02) Seat belts fastened Cooling Visors Glove heaters √Tools & Tethers clear √Gloves & HAP system Confirm GO for Translate | GEOPHYSICAL SAMPLING (00:15) Verify ALL sample IDs with sample container IDs Clean-Up Worksite √ All panels of MRU are secure and closed Stow hardware tools in MRU containment bag Stow Hardware √ Remove reel and stow antenna Transfer unused equipment to rover underseat √ Tether straps secure on all compartments on Rover Mount rover (Fasten Seatbelt) Verify following in good config. prior to commencing translation (00:02) Seat belts fastened Cooling Visors Glove heaters √Tools & Tethers clear √Gloves & HAP system Active rover from sleep mode Verify NAV states NAV RESET "RESET" - "OFF" Position LGA 0200 at Power Up Confirm GO for Translate
Variable | EV1 (CDR) | EV2 (MMP)
O2 |  | 
Pressure |  | 
EMU Faults |  | 
Water |  | 
NOTE
Check Mission Log for MCC Translation GO Criteria PRIOR to Translation
Y / N | Estimated end time:

## Slide 4
EVA – 6s: STAGE EVA – TRANSLATION TO STATION #5 (00:05)
IV | EV1 (CDR) | EV2 (MMP)
Record Observational notes when directed by EV crew Estimate time of arrival Compute estimate of minutes behind (projected minus planned arrival time) Compute estimate of timeline margin How Confident are you in your estimate (+/- min) | TRANSLATION (00:05) Correlate observation with active geophysical data Inspect targets of opportunity as appropriate Photograph and describe sample features Monitor active regolith analysis data as appropriate Correlate active data sources with observations | TRANSLATION (00:05) Operate rover along preplanned route
NOTE
In traversing from Station #4 to 5 the surface characteristics should change from the fine grained sand to a smoother mare material. Things to look for during this portion of the traverse are transition zones between sandy and mare material and their relationship to surrounding terrain and eastern edge of the debris flow. Photographic documentation of these features is desirable.
NOTE
If crew Egress to photograph sample(s) during transit. PERFORM an abbreviated systems check prior to Ingress: √Tools & Tethers clear √Gloves & HAP √Seat belts fastened √Nav System Engaged

## Slide 5
EVA – 6s: STAGE EVA – STATION #5 ACTIVITIES (00:35)
IV | EV1 (CDR) | EV2 (MMP)
Record PET at Arrival Convey summary of tasks to be performed by each crew member Confirm correct MRU ID Record number and type of samples identified for Rock sampling Confirm GO for CDR MRU activation | GEOPHYSICAL MRU EXPERIMENTS (00:35) Egress Rover Unload MRU N3 Search and Select MRU at sampling site Confirm once MRU at sampling site Configure MRU N3 (00:02) Release the 4 sensor to make contact with surface Engage deployment packet and relocate N3 components southwest of anchor point √ Remove seal protector Rotate package remove dust cover deploy anchor legs √ Obtain rammer from tool harness Level and align antenna Activate MRU N3 (00:02) Place power unit to southeast Disconnect pwr pkg from bar Reposition pwr pkg 10 ft East Remove HFE stowage pip pins Tip power package down Get camera, place on RCU Translate to 30 ft off SEQ bay √ Check for confirmation to activate MRU | GEOPHYSICAL SAMPLING (00:35) Park and Egress rover Unload Sampling MRU, camera and make Observations while photo documenting the site (00:02) Report site context description Environmental conditions (depth, current strength/direction, temperature, visibility) Unit descriptions (distinguishing features, unit relations and orientations) Variances from precursor data Other notable features Worksite Setup / Sample Prep (00:02) Set sampling markers next to candidate samples √ candidate samples are photographed Collect Rock Samples (00:05) Connect Manual Driver to Rock End Effector, pushing until Latch clicks into place Remove Manual driver and effector from Sampling MRU Squeeze and hold handle of Manual Driver while placing over sample of interest Release handle, capturing sample inside End Effector Stow End Effector in Sample MRU Repeat Sampling procedures until desired samples are collected
CAUTION
Avoid touching End Effectors to minimize contamination Trigger may kick back when attempting to engage
NOTE
Check Mission Log for MCC Activation Criteria PRIOR to Activation
WARNING
Avoid touching the upper half of the Antenna during installation so as to not damage gloves from hot surface
Sample ID | Container ID | Sample type (lvl of alt – H/M/L)

## Slide 6
EVA – 6s: STAGE EVA – STATION #5 ACTIVITIES (00:35) CONT.
IV | EV1 (CDR) | EV2 (MMP)
Confirm MRU system checkout complete Confirm each sample is collected and stowed Record number and type of samples identified for SOIL sampling Provide MCC with a quick verbal status update of activities performed at Station #4. Compute estimate of minutes behind (projected minus planned end time of Station #5 activities) Do you think the EV crew will finish Station #5 on time? If not, what is your estimated end time? Confirm GO for CDR MRU activation Confirm MRU system checkout complete | GEOPHYSICAL MRU EXPERIMENTS (00:35) Perform system checkout √ System state variables Confirm System Check Unload MRU A6 (00:02) Select and place MRU A6 at sampling site Confirm MRU A6 secured at site Configure MRU A6 (00:02) Release the 4 sensor to make contact with surface Engage deployment packet and relocate A6 SW Pull socket pin Rotate package √ remove dust cover deploy anchor legs Place secondary probes on surface √ Level and align antenna Activate MRU A6 (00:02) Place pkgs on surface with exp pkg in final position √ Disconnect pwr pkg from bar Reposition pwr pkg and Remove HFE stowage pip pins √ Tip pwr pkg down Release RTG cable B. bolts Deploy RTG cable & discard cable reel √ Check for confirmation to activate MRU Perform system checkout √ System state variables Confirm System Check | GEOPHYSICAL SAMPLING (00:35) Verify ALL sample IDs with sample container IDs Collect Soil Samples (00:02) Remove Manual Driver with Soil End Effector from Sample Briefcase Squeeze and hold handle of Manual Driver while scooping sample of interest Release handle, capturing sample inside Soil End Effector √ Stow Soil End Effector in Sample MRU container Repeat Soil Sampling procedures until desired samples are collected Verify ALL sample IDs with sample container IDs Clean-Up Worksite Stow Hardware √ All tools stowed and secured in containment bag Stow containment bag on Rover √ Tether straps secure on all compartments on Rover
CAUTION
Soil samples may leak from end effectors if seal not set
NOTE
Check Mission Log for MCC Activation Criteria PRIOR to Activation
Y / N | Estimated end time:
Sample ID | Container ID | Sample type (lvl of alt – H/M/L)

## Slide 7
EVA – 6s: STAGE EVA – STATION #5 ACTIVITIES (00:35) CONT.
IV | EV1 (CDR) | EV2 (MMP)
Confirm each sample is collected and stowed (Record Sample ID with Associated Container ID) Estimate time of departure Compute estimate of minutes behind (projected minus planned Station #5 end time) Compute estimate of timeline margin How Confident are you in your estimate (+/- min) Systems Check prior to station departure Record PET at Departure | GEOPHYSICAL MRU EXPERIMENT (00:35) Clean-Up Worksite √ MRU Systems on data collection standby mode √ All panels of MRU are secure and closed Stow hardware tools in MRU containment bag Stow Hardware √ All tools stowed and secured in containment bag Stow containment bag on Rover √ Tether straps secure on all compartments on Rover Mount rover Verify rover scientific instruments active Verify following in good config prior to commencing translation (00:02) Seat belts fastened Cooling Visors Glove heaters √Tools & Tethers clear √Gloves & HAP Confirm GO for Translate | GEOPHYSICAL SAMPLING (00:35) Mount rover Verify following in good config prior to commencing translation Seat belts fastened Cooling Visors Glove heaters Tools & Tethers clear √Gloves & HAP Active rover from sleep mode Verify NAV states NAV RESET "RESET" - "OFF" Position LGA 0200 at Power Up Confirm GO for Translate
Variable | EV1 (CDR) | EV2 (MMP)
O2 (lbs) |  | 
Pressure (psi) |  | 
EMU Faults |  | 
Water (lbs) |  | 

## Slide 8
Timeline Margin Calculation |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PET | + ETA |  | = Pred. PET |  | - Plan PET |  | = Min. Behind |  |  | Limiting Resource | - Nom End Time | = Nom. Margin | - Min. Behind | = Timeline Margin
Numerical Telemetry Events |  |  |  |  |  |  |  |  |  | Graphical Telemetry Events |  |  |  | 
PET |  | Yellow/Red (Y/R) |  | Channel |  | Variable ID |  | Value (if red) |  | PET | Variable | Channel | Trend | Value (if exceed bounds)
EVA – 6s: FLIGHT NOTES